## Slide 1: Intelligent Transmission Control Schemes for Enhancing Reliability in Vehicular Networks
Advisor: Prof. Jian-Jhih Kuo, Ph.D.
Taiwan, Fall 2022
Lan-Huong Nguyen
Dissertation presentation
Department of Computer Science and Information Engineering
College of Engineering, National Chung Cheng University

## Slide 2: Outline
Motivation & literature review
Problem identification
Our proposed methods
Evaluation results
Conclusion

## Slide 3: Motivation
Factors influence the reliability of vehicular communications
  Channel congestion
  Security attacks
Mitigating vehicular network congestion can be done by
  Increasing V2V channel bandwidth
  Utilizing resource allocation
  Controlling sending data rate
Channel congestion in V2V communications
Source: our work [2]
Our main focus
3GPP specification
Under development

## Slide 4: Literature Review (1/2)
Study | Support 5G V2X | Safety/risk factor | Fairness factor | Machine learning support | Measurement metric | Learning model
DCC [1] [12] | ✓ | ✘ | ✘ | ✘ | PDR, CBR | Linear data rate adjustment
S-DCC [9] | ✓ | ✘ | ✘ | ✓ | CBR | Fuzzy C-Mean clustering
SAE-DCC [10] | ✘ | ✘ | ✓ | ✘ | CBR | Age-of-Information Optimization
DR-DCC [15] | ✓ | ✘ | ✘ | ✓ | CBR | Deep Q-learning, K-Means
LIMERIC [14] | ✘ | ✘ | ✓ | ✘ | CBR, IPG | Adaptive data rate control
Ours | ✓ | ✓ | ✓ | ✓ | PDR, CBR, CR | Distance-risk optimization, Double Deep Q-learning

## Slide 5: Literature Review (2/2)
Our
work
Rate control for Channel Congestion Mitigation
Channel-based rate control
Collision risk rate control
ETSI DCC
(DSRC, C-V2X)
LIMERIC*
(DSRC)
RTC+
(5G V2V)
DEEPCUT
(5G V2V)
DR-DCC [15]
S-DCC [9]
SAE-DCC [10]
C-LIMERIC [15]
DBRA [15]
DR/K-means
Fuzzy C-mean
clustering
SVM
Reinforcement
Learning
*
3GPP
doesn’t
specify
to use
these

## Slide 6: Our Contributions
Two novel intelligent risk-based rate control methods to suggest the proper data rate of broadcasting V2V messages.
The vehicles can automatically adjust their sending rate based on the risk assessment. Therefore, the system can reduce the redundant sending data to mitigate the channel congestion while still maintaining the safety.
The evaluation results demonstrate the significant effects of the method in reducing the potential congestion for V2X applications, particularly maintaining safety (cut up 16% redundant data while increasing 22% packet delivery rate compared with baseline models)

## Slide 7: Problem Statement
Input: A wireless channel with limited bandwidth , N vehicles broadcasting messages
Output: A maximum number of receiver vehicles can receive data at a specific quality-of-service
Goal:
  Channel congestion mitigation
  Data transmission control without impacting safety
Challenges
  There must have an efficient mechanism to determine which vehicles are the ones to cut down their sending rate
  The safety requirement must be the priority, i.e., the vulnerable-to-collision vehicles should be prioritized to use the channel.
  Trade-off: determining a proper broadcasting rate for utilizing channel usage and guaranteeing driving safety

## Slide 8: Rate Control vs Resource Allocation
Rate control
  Manage the congestion through adjusting the sending rate of connected vehicles
Resource allocation
  Sensing-based semi-persistent scheduling (SB-SPS) manages the congestion through scheduling resource reservation interval (RRI) and power transmission for connected vehicles (
Data rate (R)=
Reduce
increase
LIMERIC

## Slide 9: System Model (1/2)
5G V2V with a fixed bandwidth
connected vehicles
At the time vehicle is sending data at a rate
= where is the number of messages vehicle sent within a time interval , e.g., 100ms.
The sum rate with N vehicles at the time t
(1)
The channel congestion occurs if >=
We don’t consider the impact of wireless path loss/interference in this work (using the simulator’s default resource allocation mechanism)
Notes: We model the V2V communications as a network with a fixed bandwidth denotes Drmax
In the network, there are N vehicles are communicating. At the time t, a vehicle I can send with a rate 〖𝐷𝑅〗_𝑖^𝑡
Accordingly, the sum data rate of N vehicles are calculated as formula in the screen
The channel congestion will occur if the sum data rate is greater than the channel capacity DRmax

## Slide 10: System Model (2/2)
Packet delivery rate (PDR) is defined as the ratio of successfully received messages to the total number of messages sent by vehicle
= (2)
where + is the number of transmitted messages by vehicle to the vehicles
+ denotes the number of messages successfully received by vehicles
within a time interval
Notes: To model the number of veh icles that can receive the V2X messages, we use the metric packet reception ratio (PRR). This metric is to measure the ratio of the successful receptions among the total number of neighbors 𝑁_𝑖^𝑡of a transmitter vehicle 𝑖. The formula as in the formula two.
In practice, a high PRR means less congestion. By contrast, a low PRR means high congestion. Recall our goal in the problem identification, our goal is to maximize PRR.

## Slide 11: Problem Formulation
The problem of network congestion mitigation is equal to the objective of the following optimization problem function:
(3)
subject to
,
,
Minimum data rate for V2X applications
Channel capacity

## Slide 12: The Key Question
  Which vehicles (low-risk or high-risk) should we reduce the sending/broadcasting rate?
V2V communications under congestion
Low-risk vehicles
High-risk vehicles
How to determine?

## Slide 13: Our Idea to Reduce Vehicles’ Sending Rate
Decrease the data rate of low-risk vehicles
Maintain the data rate of high-risk vehicles (if that is the current state)
Increase the data rate of high-risk vehicles (if the state is a transition from low risk to high risk)
Our idea is to gain two goals:
1. Help to mitigate congestion
2. Maintain the safety

## Slide 14: How to Define Collision Risk?
: the collision risk of two vehicles and at the time
= (4)
can be estimated through
  Extracting from received messages
  Self-tracking through cameras/signal-based localization
High risk vehicle: = 1
Low risk vehicle: = 0
is an expected error of distance estimation
is the threshold for a safe distance
is the distance between the vehicle and the vehicle
Example: = 72km/h (20m/s); = 2
= * = 40m
= *

## Slide 15: RTC+: Simple Risk-Based Transmission Control
Sending rate =
is the time interval
Reducing the sending rate by increasing the time interval
The parameter is an adjustable variable, = 0.9 in default
Source: our work [1]

## Slide 16: DEEPCUT: Smart DRL-based Transmission Control
We use Deep Reinforcement Learning
  Smart: Vehicles can interact with V2V communications to adjust learning strategy and broadcasting rate properly
  Efficiency: Does not require labeled datasets for training
We use the Double Deep Q-Networks (DDQN) type
  Easy to implement
  Action space is discrete so estimating max. Q-value is feasible.
Source: Lil’Log

## Slide 17: Deep Reinforcement Learning Definition (1/3)
State: Each vehicle state at the time t represents by
  Position
  Data rate
  Channel busy ratio
  For multi-agent environment
  = {, …., }
Action: Each vehicle takes an action to adjust
  = {, 0, }
is the step change for the sending rate
Our DDQN-based model architecture
Notes: In Deep Reinforcement learning, the definition of state/action and policy plays a critical role. We define its state and action space as follows.
Every vehicle state 𝑠_𝑖^𝑡 at the time t includes three elements (Position, Data rate, channel busy rate). For multi-agent environment, we can merge the state of N vehicles into one vector 𝑠^𝑡
The action space includes three values {−𝛽, 0, 𝛽} , where 𝛽 is the step change for the sending rate 〖𝐷𝑅〗_𝑖^𝑡

## Slide 18: Deep Reinforcement Learning Definition (2/3)
The problem of network congestion mitigation is equal to the objective of the following optimization problem function:
subject to
,
,
where is the reward for the action
is the discount factor
The goal of the DRL-based optimization problem is to optimize the policy to maximize the cumulative reward values, i.e., total number of all transmitter vehicles’ neighbors that can decode the messages at time .
(5)

## Slide 19: Deep Reinforcement Learning Definition (3/3)
Reward
(6)
is the CBR threshold to
determine the channel busy, e.g., = 0.85 (85%).
The value of a, b, c, d are adjustable values but should be proportional to the state of the channel and risks
- The higher risk + congestion the action causes, the higher penalty it gets (negative value)
- For example, a=-10, b=-2, c=-4, d = 2

## Slide 20: DDQN-based Transmission Control Algorithm
DDQN-based transmission control architecture
Multi-agent model to make a consensus decision

## Slide 21: DDQN-based Transmission Control Algorithm
Source: our work [2]
Workflow
DDQN-based learning model is trained on the congested/heavy traffic cases in an offline training
Each vehicle is equipped with a pre-trained DDQN-based model
The DDQN-based rate control will adjust the sending rate based on its assessment on the channel (RIS, CBR) at the time
2
1
3
Notes: This is the detail of the workflow for our DDQN-based model.
After the DDQN model is trained, it will be equipped into the vehicle’s onboard units.
Once the vehicle faces a congestion/heavy traffic case (for example, CBR is greater than a threshold), the system will launch the risk assessment and adjust the sending rate 〖𝐷𝑅〗_𝑖^𝑡 accordingly.
As illustrated in the workflow, the performance of our system will depend on the performance of two components: risk assessment and the DDQN-pre-trained model. In this work, we use time-to-collision and distance to measure the risk since they are simple and easy to implement. In the future, more methods can be extended based on this approach.

## Slide 22: Centralized vs Decentralized
Centralized method: Road-side unit to play the role of data rate control
Advantage
  Fast learning convergence
  Easy to adjust hyperparameters
Disadvantage
  Require centralized server connections (V2I), e.g., cloud server, road side units
  Challenge to deploy in the areas without core network infrastructure
Decentralized method: Vehicles negotiate with each other to determine the data rate
Advantage
  Work well with V2V environments
Disadvantage
  Slower learning convergence
  Difficult to maintain the consistency of learning models for vehicles with different computation capabilities.
Suitable for rural areas
Suitable for urban areas

## Slide 23: Evaluation Results
Ours
DSRC rate control
C-V2X/DSRC rate control
System configuration
Simulator: Veins, OpenCV2X
Adjust the broadcasting rate based on
the CBR level, regardless of risk/no-risk states

## Slide 24: Measurement Metric
Packet Delivery Rate
 the ratio of successfully received messages to the total number of messages sent
Channel Busy Ratio
 the ratio of time that the channel has been sensed busy in a given time window T
Collision risk
 the total times each pair of vehicles exceeds the safe distance at their relative speed
Computing time
 The latency of suggesting a proper broadcasting rate adjustment once the congestion occurs
V2V communication standard
  IEEE 802.11p: 5.9GHz
  5G C-V2X NR: 40GHz
V2X communication scenario
  Heavy traffic (5-10 vehicles broadcasting)
   200 vehicles/km
  Network congestion (> 20 vehicles broadcasting)
   300 vehicles/km
Luxembourg SUMO Traffic
(mobility model follows real traffic patterns)

## Slide 25: Result – DDQN training
The training converges after 2500 episodes
If we set a high timestep and replay memory (large exploration), the training convergence is expected to be longer than this result
Source: from our work [2]

## Slide 26: Packet Delivery Rate performance
DEEPCUT yields 22.63% PDR performance better than DCC/LIMERIC with TX-RX distance < 200m
If the TX-RX distance > 200m (far distance), collision risk is less critical  high cut + poor communication for far distance  low PDR but OK
Advantage of DEEPCUT:
  Hundreds of thousands of trial-and-fail training to find the best sending rate for multiple vehicle (multi-agent DRL)
Source: from our work [2]
Heavy traffic
Congested channel

## Slide 27: Channel Busy Ratio performance
DEEPCUT maintains 20% better performance in overall CBR
If traffic jam occurs ( after 150th seconds), the risk of slow-moving vehicles is low  an aggressive rate control like ours can significantly reduce the CBR
Source: from our work [2]
Congested channel
Heavy traffic
150th

## Slide 28: Collision risk performance
DEEPCUT/RTC+ can reduce average 21% less collision risk in all the cases of traffic density
Our risk-based assessment model contributed positive results
Collision risk still occurs in some cases, if traffic jam or group vehicles moving near each others  we didn’t control the vehicle behavior in this work
Source: from our work [2]
Heavy traffic
Congested channel
~21%

## Slide 29: Computing Time performance
DEEPCUT gives the highest computing time, particularly to support many vehicles
  Hard to find the consensus
  Include the extensive computation (risk assessment)
Computing time is still acceptable
  Many V2X road-safety apps can accept latency up to 100ms [5]
  In the future, computers in vehicles will be much stronger
  The case of 300 vehicles per km is not common
Source: from our work [2]
The most
common
case
The
rare
case

## Slide 30: Conclusion
Two novel intelligent control schemes are efficient to resolve the channel congestion in V2V communications while still maintaining the safety proportionally.
The risk factor is an advantage of our methods. It can help to the rate control to know exactly which vehicles should reduce the sending rate.
Ongoing work: Support the fairness index in data rate control
Future work: We move to support aerial vehicular communications, given their prospective to be deployed in 6G networks

## Slide 31: Publication Overview
Lan-Huong Nguyen, Van-Linh Nguyen, and Jian-Jhih Kuo, “Risk-Based Transmission Control for Mitigating Network Congestion in Vehicle-to-Everything Communications,” IEEE Access, vol. 9, pp. 144469-144480, Oct. 2021
Lan-Huong Nguyen, Van-Linh Nguyen, and Jian-Jhih Kuo, “Efficient Reinforcement Learning-based Transmission Control for Mitigating Channel Congestion in 5G V2X Sidelink,” IEEE Access, vol. 10, pp. 62268 - 62281, Jun. 2022
Lan-Huong Nguyen, Ren-Hung Hwang, Po-Ching Lin, Van-Linh Nguyen, and Jian-Jhih Kuo, ”Robust Positioning-based Verification Scheme for Enhancing Reliability of Vehicle Platoon Control,” in IEEE Vehicular Technology Conference (VTC), Sep. 2021
Yun-Hao Ye, Zhi-Yang Lin, Chih-Chiung Yao, Lan-Huong Nguyen, Jian-Jhih Kuo, and Ren-Hung Hwang “Efficient Multi-maneuver Platooning Framework for Autonomous Vehicles on Multi-lane Highways” in IEEE Vehicular Technology Conference (VTC), Sep. 2021.
Van-Linh Nguyen, Lan-Huong Nguyen, Jian-Jhih Kuo, Po-Ching Lin, Ren-Hung Hwang “Intelligent Aerial Relay Deployment for Enhancing Connectivity in Emergency Communications,” IEEE Transactions on Vehicular Technology (Major revision)
Van-Linh Nguyen, Lan-Huong Nguyen, Jian- Jhih Kuo, Ren-Hung Hwang, Po-Ching Lin,” Efficient Aerial Relaying Station Path Planning for Emergency Event-based Communications”, accepted to appear in IEEE CCNC 2023, Jan 2023.

## Slide 32: Reference
S. Kühlmorgen, H. Lu, A. Festag, J. Kenney, S. Gemsheim, and G. Fettweis, “Evaluation of congestion-enabled forwarding with mixed data traffic in vehicular communications,” IEEE Transactions on Intelligent Transportation Systems, vol. 21, no. 1, pp. 233–247, 2020.
G. Thandavarayan, M. Sepulcre, and J. Gozalvez, “Cooperative perception for connected and automated vehicles: Evaluation and impact of conges- tion control,” IEEE Access, vol. 8, pp. 197 665–197 683, 2020.
S. Husain, A. Kunz, A. Prasad, E. Pateromichelakis, K. Samdanis, and J. Song, “The road to 5G V2X: Ultra-high reliable communications,” in 2018 IEEE Conference on Standards for Communications and Networking (CSCN), 2018, pp. 1–6.
H. Zhou, W. Xu, J. Chen, and W. Wang, “Evolutionary V2X technologies toward the internet of vehicles: Challenges and opportunities,” Proceeding of IEEE, vol. 108, no. 2, pp. 309–323, 2020.
3GPP.TR.22.886, “Study on enhancement of 3gpp support for 5G V2X services,” 3GPP TR 22.886 V16.1.1 (2018-09), 2018.
R. Liu, J. Wang, and B. Zhang, “High definition map for automated driving: Overview and analysis,” The Journal of Navigation, vol. 73, no. 2, pp. 324–341, 2020.
5GAA, “V2X functional and performance test procedures – selected assessment of device to device communication aspects,” 5G Automotive Association, 2018.
3GPP, “Study on LTE-based V2X services (v14.0.0, release 14),” Techni- cal Specification Group Radio Access Network, 2016

## Slide 33: Reference
P. Sewalkar and J. Seitz, “Mc-coco4v2p: Multi-channel clustering-based congestion control for vehicle-to-pedestrian communication,” IEEE Transactions on Intelligent Vehicles, pp. 1–1, 2020.
N. Lyamin, B. Bellalta, and A. Vinel, “Age-of-information-aware decentralized congestion control in VANETs,” IEEE Networking Letters, vol. 2, no. 1, pp. 33–37, 2020.
C. Belagal Math, H. Li, S. Heemstra de Groot, and I. G. Niemegeers, “V2X application-reliability analysis of data-rate and message-rate congestion control algorithms,” IEEE Communications Letters, vol. 21, no. 6, pp. 1285–1288, 2017.
ETSI, “Intelligent transport systems (ITS);decentralized congestion control mechanisms for intelligent transport systems operating in the 5 GHz range; access layer part,” ETSI TS 102 687 V1.2.1, 2018.
——, “Intelligent transport systems (its); vehicular communications; basic set of applications; part 2: Specification of cooperative awareness basic service,” ETSI - EN 302 637-2, 2014.
G. Bansal, J. B. Kenney, and C. E. Rohrs, “Limeric: A linear adaptive message rate algorithm for dsrc congestion control,” IEEE Transactions on Vehicular Technology, vol. 62, no. 9, pp. 4182–4197, 2013.
A. Balador, E. Cinque, M. Pratesi, F. Valentini, C. Bai, A. A. Gómez, and M. Mohammadi, “Survey on decentralized congestion control methods for vehicular communication,” Vehicular Communications, vol. 2021, p. 100394, 2021

## Slide 34: Thank you for listening!
Notes: Thank you for listening my dissertation presentation.
If you have any questions on our work, please let me know.
Thank you professors.

## Slide 35: Ongoing work
If there are so many vehicles with the same risk assessment level, how to manage the fairness in cutting data for all vehicles?
This part is addressed in our ongoing work which partially submitted to ICC 2023 for reviewing
Platooning
Mixed traffic case

## Slide 36: Support fairness assessment factor
We supply the fairness index
Jain’s fairness index of data rate for all vehicles is defined as follows:
=
This fairness index varies in accordance with the number of vehicles and the achieved data rate. Given that multiple vehicles can be in the same group of high-risk/low-risk assessment, cutting the sending rate or lengthening the time interval for any vehicle should be flexibly adjusted to maintain the fairness of QoS gains for all vehicles of the group.
(6)

## Slide 37: Rewritten problem statement
The goal is to adjust the number of messages that transmit from vehicles or the time interval for maximizing packet delivery rate of each vehicle . This target is equal to the objective of the following optimization problem function
Where is the minimum Jain’s fairness index value.
(7)
Update this constraint

## Slide 38: Updated Deep Reinforcement Learning
The problem of network congestion mitigation is equal to the objective of the following optimization problem function:
subject to
,
,
3. ,
where is the reward for the action
(8)
Update this constraint

## Slide 39: Some performance comparison (1/2)
F-RTC : Fairness Risk-based Transmission Control
Performance comparison
Reward accumulation
Packet Delivery Rate
Channel Busy Ratio
Collision risk

## Slide 40: Some performance comparison (2/2)
F-RTC : Fairness Risk-based Transmission Control
F-RTC/DEEPCUT: 50-80ms
Others: 90-120ms
Shorter time interval is better